## Slide 1: 19CS2109
COMPUTER NETWORKS AND SECURITY
© 2020-21 KL University – The contents of this presentation are an intellectual and copyrighted property of KL University. ALL RIGHTS RESERVED

## Slide 2: Introduction
Session-4
© 2020-21 KL University – The contents of this presentation are an intellectual and copyrighted property of KL University. ALL RIGHTS RESERVED

## Slide 3: Network Hardware
Local Area Networks
Metropolitan Area Networks
Wide Area Networks
Wireless Networks
Home Networks
Internetworks

## Slide 4
Types of transmission technology
Broadcast links
Point-to-point links
Network Hardware

## Slide 5
Network Hardware
  Broadcast networks
    single communication channel shared by all machines
    broadcasting or multicasting (via packets)
      broadcasting: a special code in address field
      multicasting: reserve one bit to indicate multicasting, the remaining n-1address bits can hold a group number. Each machine can subscribe to any groups
    used by localized networks (or satellites)
  point-to-point networks
    many hops
    routing algorithms: multiple routs are possible
    used by large networks

## Slide 6: Classification of interconnected processors by scale

## Slide 7: Local Area Networks (LANs)
Two broadcast networks
(a) Bus
(b) Ring
· Characterics of LANs: (a) privated-owned, (b) small size,
(c) transmission technology, (d) topology
· Ethernets are most popular (up to 10 Gb/s)

## Slide 8: Local Area Networks
Characteristics
  small size
  transmission technology
    single cable
    10Mbps ~ 10Gb/s
    10Gb/s : 10,000,000.000 bps
  topology:
    bus
      Ethernet (IEEE 802.3): 10 or 100 Mbps (10Gb/s)
    ring
      IBM token ring (IEEE 802.5): 4 or 16 Mbps
Channel allocation of broadcast networks
  static: each machine has an allocated time slot
  dynamic

## Slide 9: Metropolitan Area Networks
A metropolitan area network based on cable TV.

## Slide 10: Wide Area Networks (WANs)
Relation between hosts on LANs and the subnet.
·WANs are point-to-point networks
·WANs consist of two distinct components:
transmission lines (copper, fiber, microwave) and switches (electronics, optics)
 Store-and-forward or packet-switched subnet

## Slide 11
Network Topology

## Slide 12: Subnet (WANs)
Subnet (WANs) is consists of two components:
  transmission lines (circuits, channels, trunks)
    move bits between machines
  switching elements
    connect transmission lines
    Router: also called packet switching nodes, intermediate systems, and data switching exchanges
    Operate in store-and-forward, or packet-switched mode.

## Slide 13: Wide Area Networks (2)
A stream of packets from sender to receiver. (virtual- circuit)
Routing decisions are made locally·
How A makes that decision is called the routing algorithm.
 Will be studied in detail in Chapter 5.
9/17 End

## Slide 14: Wireless Networks
Categories of wireless networks:
System interconnection
(short-range radio, e.g. Bluetooth)
Wireless LANs
(802.11a, 802.11b, 802.11g)
Wireless WANs
(802.16, Cellular telephones, Satellites)
Wireless sensor networks

## Slide 15: Wireless Networks (2)
(a) Bluetooth configuration
(b) Wireless LAN

## Slide 16: Wireless Networks (3)
(a) Individual mobile computers
(b) A flying LAN

## Slide 17: Home Network Categories
Computers (desktop PC, PDA, shared peripherals)
Entertainment (TV, DVD, VCR, camera, stereo, MP3)
Telecomm (telephone, cell phone, intercom, fax)
Appliances (microwave, fridge, clock, furnace, airco., light)
Telemetry (utility meter, smoke/burglar alarm, babycam).

## Slide 18
Fundamentally different properties
1. Devices have to be easy to install
2. The network and devices have to be foolproof in
operation
3. Low price is essential
4. The network needs sufficient capacity ( for multimedia
application)
5. The network interface and wiring have to be stable for
many years
6. Security and reliability will be very important
(minimize false alarm or misalarm)
Home networks may be wired or wireless

## Slide 19: Internetworks
Internetworks connect networks with different hardware
and software
A collection of interconnected networks is called
an internetwork or internet
Internet is one specific internet
Gateways are used to make the connection and to
provide the necessary translation (protocol convertion)

## Slide 20: Network Software
Protocol Hierarchies (Layer structure)
Design Issues for the Layers
Connection-Oriented and Connectionless Services
Service Primitives
The Relationship of Services to Protocols

## Slide 21: Network Software
Protocol Hierarchies
  a series of layers (levels)
  lower layer provides service to higher layers
  protocol:
    an agreement between the communication parties on how communication is to proceed
  Peers:
    the corresponding layers on different machines.
  Network architecture: a set of layers and protocols
  Protocol stack:
    a list of protocols used by a certain system, one protocol per layer

## Slide 22: Network Software Protocol Hierarchies
Layers, protocols, and interfaces.
 Peer
Network Architecture: A set of layers and protocols
Protocol Stack: A list of protocols used by a certain system, one protocol per layer.
Virtual
Communication
Physical
Communication

## Slide 23
◆ Layering
➭ To make things simple: modularization
➭ Different layer has different functions
➭ Create layer boundary such that
● description of services can be small
● number of interactions across boundary are minimized
● potential for interface standardized
➭ Different level of abstraction in the handling of data (e.g.,
syntax, semantics)
➭ Provide appropriate services to upper layer
➭ Use service primitives of lower layer
Network Software

## Slide 24: Protocol Hierarchies (2)
The philosopher-translator-secretary architecture.

## Slide 25: Protocol Hierarchies (3)
Example information flow supporting virtual communication in layer 5.
Message segmentation
Encapsulation

## Slide 26: Design Issues for the Layers
Addressing (telephone number, e-mail address, IP address,…)
Error Control (error correction codes, ARQ, HARQ,…)
Flow Control (feedback-based, rate-based)
Multiplexing (gathering several small messages with the same destination into a single large message or vice versa  Demultiplexing)
Routing (directing traffic to the destination)

## Slide 27
Design Issues for Layers
Identify senders and receivers
  multiple computers and processes: addressing
Data transfer
  simplex, half-duplex, full-duplex communication
  # of logical channels per connections, priorities
Error control
  error detection
  error correction
Sequencing of pieces

## Slide 28
Design Issues for Layers
Flow control
  feedback from the receiver
  agreed upon transmission rate
Length of messages
  long messages: disassemble, transmit, and reassmeble messages
  short messages: gather several small messages
Multiplexing and Demultiplexing
  when expensive to set up a separate connection
  needed in physical layer
Routing: split over two or more layers
  High level: London -> France or Germany -> Rome
  Low level: many available circuits

## Slide 29: Connection-Oriented and Connectionless Services
Six different types of service.

## Slide 30: Service Primitives (Operations)
Five service primitives for implementing a simple connection-oriented service.
A service is formally defined by a set of primitives (operations) available to a user process to access the services.

## Slide 31: Service Primitives (2)
Packets sent in a simple client-server interaction on a connection-oriented network.
If the protocol stack is located in the operating system,
the primitives are normally system calls.

## Slide 32: Services to Protocols Relationship
The relationship between a service and a protocol.
·The service defines what operations the layer is prepared to perform on behalf of its users
·A service is a set of primitives that a layer provides to the layer above it.
·A protocol is a set of rules governing the format and meaning of the packets which are
exchanged by the peer entities in the same layer.
Service Providers
Service Users
Services related to the interfaces between layers;
Protocols related to the packets sent between peer entities on different machine.